## Slide 1: Communication in embedded systems
Week 8
Synchronization with Queues

## Slide 2: Why are Mutexes not always enough?
We can have a situation where threads must wait for a longer, unpredictable time
  Suppose you have buffer, and must wait because the buffer is full
Mutexes are not meant for that
We can use one of the other synchronization primitives;
  Queues
  Semaphores
  Notifications

## Slide 3: Queues
FreeRTOS was designed to have a small ROM footprint, therefore:
  All event management functionality is built into the Queue data structures (contrary to most other RTOS designs)
  The Queue mechanism is used to implement:
    Queues themselves
    Mutexes
      Implemented as macros that use Queues, introducing some new code
    Semaphores
      Implemented as macros that use Queues, introducing no new code

## Slide 4: Queue concept
A Queue can contain a limited number of messages of fixed size
Basically just 2 methods: put and get
Can be called from thread and from ISR
This is not a FIFO queue
  put puts a message in the Queue, based on its priority
  When messages have equal priority, the FIFO

## Slide 5: Queue synchronization
There are some situations where synchronization is required:
  2 threads calling put and/or get at the same time
    These calls will be executed one by one
    Similar as for Mutexes
  Thread(s) calling put while the buffer is full
    Each thread will get blocked
    Other thread(s), calling get, will wake them up one by one (highest priority first)
  Threads calling get while the buffer is empty
    Each thread will get blocked
    Other thread(s), calling put, will wake them up one by one (highest priority first)

## Slide 6: Queues API
We have these basic functions:
  osMessageQueueNew
  osMessageQueuePut
  osMessageQueueGet
Some extra functions:
  osMessageQueueReset
  osMessageQueueDelete
And some getters:
  osMessageQueueGetName
  osMessageQueueGetCapacity
  osMessageQueueGetMsgSize
  osMessageQueueGetCount
  osMessageQueueGetSpace

## Slide 7: Creating a Queue osMessageQueueNew
When we create a new Queue, we must specify:
  The number of messages that the Queue can contain (for example: 5)
  The size of each message in bytes (for example: 4 or sizeof(int))
  Some attributes (can often be left at default values):
    typedef struct {
    const char *name; // for debugging purposes; default NULL
    uint32_t attr_bits; // attribute bits; not used; default 0
    void *cb_mem; // memory for control block; default NULL
    uint32_t cb_size; // size of memory for control block; def 0
    void *mq_mem; // memory for data storage; default NULL
    uint32_t mq_size; // size of memory for data storage; def 0
    } osMessageQueueAttr_t;

## Slide 8: Adding a message osMessageQueuePut
When we add a message to a Queue, we must specify:
  The ID of the Queue (returned by osMessageQueueNew)
  Pointer to a buffer that contains the message
  Priority of the message (defines which place it gets in the Queue)
  Timeout value in kernel ticks
Note: the whole message is copied from the buffer to the Queue

## Slide 9: Taking a message osMessageQueueGet
When we add a message to a Queue, we must specify:
  The ID of the Queue (returned by osMessageQueueNew)
  Pointer to a buffer where the message will be stored
  Pointer to priority of the message
  Timeout value in kernel ticks
Note: the whole message is copied from the buffer to the Queue

## Slide 10: Queue example

## Slide 11: Pros & Cons for Mutex
Pros
  Easy to use
  A good solution in many cases
Cons
  Can not be used from ISR’s
  Not good for every situation

## Slide 12: Assignment 5
Extend your program to also receive data from the PC
Each character received by the device must be increased and sent back to the PC; e.g.:
  When the user types ‘4’ on the PC, your device must return ‘5’
  When the user types ‘d’ on the PC, your device must return ‘e’
Do this again in 2 ways:
  Use the “normal” Serial library to receive/send data from/to your PC
  Receive/send the same data without using Serial, but by directly accessing the UART registers (UDR, UCSR, UBRR)
Try out how much you can change the baud rate before you start getting errors
Make sure that you can explain clearly
  How you initialized the UART
  How receiving and transmitting works